BUSINESS COMMUNICATIONS

MANAGER 50

SYSTEM COORDINATOR INSTRUCTIONS VIA THE TELEPHONE

SMISTON COMMUNICATIONS

133 MANITOU DR.

KITCHENER, ON  N2C 1L4

PHONE: 519-748-2226

FAX:  519-748-0061

TELEPHONE SYSTEM INSTRUCTIONS FOR BCM 50 VIA THE PHONE

TABLE OF CONTENTS

PROGRAMMING OVERLAY							PAGE 3

TIME & DATE CHANGE 							PAGE 4

CUSTOMIZING YOUR TELEPHONE 					PAGE 5

BUTTON INQUIRY 								PAGE 5

PROGRAMMING EXTERNAL #’S 						PAGE 5

PROGRAMMING INTERNAL #’S 						PAGE 5

PROGRAMMING FEATURE CODES 					PAGE 6

NAMING AN EXTENSION 							PAGE 6

ASSIGNING LINE APPEARANCES 						PAGE 7

CALL FORWARD NO ANSWER 						PAGE 8

CALL FORWARD ON BUSY							PAGE 9

SYSTEM SPEED DIALS 							PAGE 10

SET RELOCATION 								PAGE 11

TO CHANGE AN EXTENSION 						PAGE 12

TELEPHONE FEATURES 							PAGE 13

PROGRAMMING OVERLAY

THIS PROGRAMMING OVERLAY IS USED FOR EITHER THE M-SERIES PHONES OR THE T-SERIES PHONES

| HEADING | ▲ ▲ | SHOW |
| --- | --- | --- |
| BACK | ▲ ▲ | NEXT |

NOTE:  WHEN YOU GO INTO PROGRAMMING THERE ARE 3 ARROWS THAT LIGHT UP AND THEY LOOK LIKE THE ONES ABOVE.  EACH ARROW TAKES ON A FUNCTION WHILE IN PROGRAMMING.

NOTE:  IN THE DOCUMENTATION FOR INSTRUCTIONS IT IS REFERENCED TO PRESS THE TOP RIGHT ARROW, BOTTOM RIGHT ARROW, TOP LEFT ARROW AND BOTTOM LEFT ARROW

TIME CHANGE FOR BCM 50 SYSTEM:

Using Card Board Overlay (attached to this sheet)

Press Feature * * 266344

User ID: 738662 and press OK

Screen Shows: Password

Enter 266344 and press OK

Screen will then display: Terminals & Sets

Press the Next (bottom right arrow) Button until the screen displays: Time & Date

Press the Show (top right arrow) Button

Screen will then display: HOUR:____ with the option to choose Next or Change

To change the Hour press the Change Button and enter in the hour (ex.  01, 10, 12)

Screen will then prompt you to choose AM or PM

Press the Next (bottom right arrow) Button

Screen will then display: MINUTES: _____ with the option to choose Next or Change

To change the Minutes press the Change Button and enter in the minutes (ex. 25, 02, 13)

Press the Next (bottom right arrow) Button

Screen will then display: YEAR: _____ with the option to choose Next or Change

To change the Year press the Change Button and enter in the year (ex. 05, 02)

Press the Next (bottom right arrow) Button

Screen will then display: MONTH: ____ with the option to choose Next or Change

To change the Month press the Change Button and enter in the month (ex. 01, 12)

Press the Next (bottom right arrow) Button

Screen will then display: DAY: _____ with the option to choose Next or Change

To change the Day press the Change Button and enter in the day (ex. 01,31)

Press the Next (bottom right arrow) Button, Then press the RLS Button

CUSTOMIZING YOUR TELEPHONE:

FINDING OUT WHAT A BUTTON DOES USING “BUTTON INQUIRY”

-PRESS FEATURE (GREY NORTEL SYMBOL) * 0 (ZERO)

-PRESS THE BUTTON YOU WOULD LIKE TO KNOW THE FUNCTION OF

***NOTE*** TO DETERMINE WHAT EXTENSION # A PHONE IS, DO THE FOLLOWING STEPS ABOVE AND PRESS THE “INTERCOM” BUTTON

-PRESS RLS (RELEASE) ONCE YOU ARE DONE

TO PROGRAM AN EXTERNAL # ON YOUR TELEPHONE:

-PRESS FEATURE (GREY NORTEL SYMBOL) * 1

-CHOOSE THE BUTTON YOU WOULD LIKE TO PROGRAM ON

-ENTER THE “TELEPHONE #” AND PRESS THE # SIGN TO ACCEPT

***NOTE*** IF YOU HAVE TO DIAL “9” TO GET AN OUTSIDE LINE THAN DO THE FOLLOWING BELOW:

-PRESS FEATURE (GREY NORTEL SYMBOL) * 1

-CHOOSE THE BUTTON YOU WANT TO PROGRAM ON

-PRESS THE “INTERCOM” BUTTON AND ENTER “9”

-ENTER THE “TELEPHONE #” AND PRESS THE # SIGN TO ACCEPT

TO PROGRAM AN INTERNAL # ON YOUR TELEPHONE:

-PRESS FEATURE (GREY NORTEL SYMBOL) * 2

-CHOOSE THE BUTTON YOU WOULD LIKE TO PROGRAM ON

-ENTER THE “EXTENSION #” YOU WANT TO PROGRAM AND PRESS THE #

SIGN TO ACCEPT

TO PROGRAM A FEATURE CODE ON YOUR TELEPHONE:

-PRESS FEATURE (GREY NORTEL SYMBOL) * 3

-CHOOSE THE BUTTON YOU WOULD LIKE TO PROGRAM ON

-ENTER THE “FEATURE CODE” YOU WOULD LIKE

CHANGING THE NAME OF AN EXTENSION:

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE “EXTENSION #” YOU WANT TO NAME

-PRESS “SHOW” (TOP RIGHT ARROW)

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “NAME”

-PRESS “CHANGE” TO CHANGE THE NAME OR “CLR” TO CLEAR IT

(TO GET A SPACE, PRESS THE # SIGN ONCE, TO GET A COMMA, PRESS THE # SIGN TWICE)

-WHEN YOU ARE FINISHED PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE USER PREFERENCES

-PRESS “HEADING” 2 TIMES UNTIL YOU SEE “TERMINALS & SETS”

-PRESS RELEASE OR HANG UP, WAIT A COUPLE MINUTES FOR THE CHANGES TO UPDATE.

ASSIGNING LINES ON A TELEPHONE SET:

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE “EXTENSION #” YOU WANT TO CHANGE

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SHOULD SAY “LINE ACCESS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SAYS “LINE ASSIGNMENT”

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SAYS “SHOW LINE:___”

-ENTER THE LINE # (IE. 001, 002)

-SCREEN WILL TELL YOU WHAT IT IS SET AT

-IF YOU WANT IT TO BE APPEAR ONLY, RING ONLY, APPR & RING, UNASSIGNED YOU MUST PRESS “CHANGE” UNTIL YOU SEE WHAT YOU WANT

-PRESS “HEADING” (TOP LEFT ARROW)

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE NEXT LINE # AND FOLLOW THE SAME STEPS ABOVE

-REPEAT FOR EACH LINE & ONCE FINISHED PRESS RELEASE OR HANG UP

-WAIT A FEW MINUTES FOR THE SYSTEM TO UPDATE

TO CHANGE/ADD CALL FORWARD NO ANSWER:

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) 985, WRITE DOWN THE # THAT YOU SEE AND PRESS “OK”

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE “EXTENSION #” YOU WANT TO CHANGE

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SHOULD SAY “LINE ACCESS”

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “CAPABILITIES”

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SHOULD SAY “FWD NO ANSWER”

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SAYS “FWD TO: NONE, CHANGE” OR “FWD TO: WITH A #, CHANGE”

-TO “REMOVE” THE CALL FORWARD, PRESS “CLR”

-PRESS “CHANGE” TO ENABLE CALL FORWARD NO ANSWER, AND ENTER THE VOICEMAIL # THAT YOU WROTE DOWN AT THE BEGINNING OF THESE INSTRUCTIONS

-PRESS “NEXT” (BOTTOM RIGHT ARROW)

-SCREEN SAYS “FORWARD DELAY: 4, CHANGE”

-THIS IS WHERE YOU CAN “CHANGE” THE # OF RINGS THAT PHONE RINGS BEFORE IT GOES INTO VOICEMAIL

-TO “CHANGE” THE # OF RINGS, PRESS “CHANGE” UNTIL YOU SEE THE AMOUNT OF RINGS YOU WANT

-PRESS “NEXT” (BOTTOM RIGHT ARROW)

-PRESS “HEADING” 4 TIMES AND THEN PRESS RELEASE OR HANG UP

-WAIT A FEW MINUTES FOR THE SYSTEM TO UPDATE

TO CHANGE/ADD CALL FORWARD ON BUSY:

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) 985, WRITE DOWN THE # THAT YOU SEE AND PRESS “OK”

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE “EXTENSION #” YOU WANT TO CHANGE

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SHOULD SAY “LINE ACCESS”

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “CAPABILITIES”

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SHOULD SAY “FWD NO ANSWER”

-PRESS “NEXT” (BOTTOM RIGHT ARROW)

-SCREEN SAYS “FWD ON BUSY”

-PRESS “SHOW” (TOP RIGHT ARROW)

-TO “CHANGE” PRESS “CHANGE” AND ENTER THE VOICEMAIL # THAT YOU WROTE DOWN AT THE BEGINNING OF THIS

-TO “REMOVE” THE CALL FORWARD ON BUSY PRESS “CHANGE” AND IT SHOULD SAY “FWD TO: NONE”

-PRESS “NEXT” (BOTTOM RIGHT ARROW)

-PRESS “HEADING” 4 TIMES AND THEN PRESS RELEASE OR HANG UP

-WAIT A FEW MINUTES FOR THE SYSTEM TO UPDATE

ADDING/CHANGING SYSTEM SPEED DIALS:

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “SYS SPEED DIAL”

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE SPEED DIAL # YOU WOULD LIKE TO PROGRAM A TELEPHONE # ON (IE. 01, 02)

-PRESS “SHOW” (TOP RIGHT ARROW)

-SCREEN SAYS: “01:NO NUMBER, CHANGE” OR IT MAY HAVE A # ALREADY PROGRAMMED

-PRESS “CHANGE” TO “ADD” OR “DELETE” A TELEPHONE #

-TO “ADD” PRESS “CHANGE” AND ENTER THE TELEPHONE # AND PRESS “OK”

-PRESS “HEADING” (TOP LEFT ARROW)

-PRESS “NEXT” (BOTTOM RIGHT ARROW)

-ENTER ANOTHER SPEED DIAL # AND REPEAT THE STEPS ABOVE

-PRESS “HEADING” 2 TIMES AND THEN PRESS RELEASE OR HANG UP

-WAIT A FEW MINUTES FOR THE SYSTEM TO UPDATE

SET RELOCATION

TO MOVE A PHONE FROM ONE JACK TO ANOTHER AND KEEP THE EXTENSION AND ALL THE PROGRAMMING:

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “SYSTEM PRGRMING”

-PRESS “SHOW” (TOP RIGHT ARROW)

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “FEATR SETTINGS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “SET RELOCATION:Y OR N, CHANGE

-PRESS “CHANGE” TO TURN IT ON, Y FOR YES

-PRESS “CHANGE” TO TURN IT OFF, N FOR NO

-PRESS “HEADING” 2 TIMES AND THEN PRESS RELEASE OR HANG UP

-WAIT A FEW MINUTES FOR THE SYSTEM TO UPDATE

TO CHANGE AN EXTENSION : (Please note this is only to change an extension # to another extension #, ie. Ext. 251 to Ext. 256

-USING YOUR PROGRAM OVERLAY ON 1ST PAGE, PLACE OVER A PROGRAMMING PHONE (A PHONE WITH A SCREEN & 3 TOGGLE BUTTONS UNDERNEATH)

-PRESS FEATURE (GREY NORTEL SYMBOL) * * 266344

-USER ID IS: 738662 AND PRESS OK

-PASSWORD IS: 266344 AND PRESS OK

-SCREEN SHOWS, “TERMINALS & SETS”

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “SYSTEM PRGRMING”

-PRESS “SHOW” (TOP RIGHT ARROW)

-PRESS “NEXT” (BOTTOM RIGHT ARROW) UNTIL YOU SEE “CHANGE DNS”

-PRESS “SHOW” (TOP RIGHT ARROW)

-ENTER THE “OLD DN” EXT #, THEN ENTER THE “NEW DN” EXT #

-PRESS “HEADING” 2 TIMES AND THEN PRESS RELEASE OR HANG UP

-WAIT A FEW MINUTES FOR THE SYSTEM TO UPDATE

TELEPHONE FEATURES

SOFTKEYS:

THESE ARE THE 3 TOGGLE BUTTONS BELOW YOUR SCREEN ON YOUR PHONE.

NOTE: THE FOLLOWING 5 FEATURES BELOW ARE ONLY AVAILABLE IF YOU HAVE A MAILBOX OR VOICEMAIL ON YOUR PHONE.

SEND A MSG: (FEATURE 980)

TO LEAVE SOMEONE IN THE OFFICE A VOICEMAIL MESSAGE.

PRESS THE LEAVE MSG BUTTON AND ENTER IN THE MAILBOX # OF THE

PERSON YOU WISH TO LEAVE A MESSAGE FOR.  RECORD YOUR MESSAGE

AND THEN YOU MUST PRESS THE SOFT KEY THAT SAYS SEND FOR THE

MESSAGE TO BE DELIVERED.

OPEN MAILBOX: (FEATURE 981)

TO OPEN YOUR MAILBOX AND RETRIEVE YOUR MESSAGES

PRESS THE OPEN VM BUTTON THEN ENTER IN YOUR PASSWORD AND

PRESS OK.

FWD TO VM: (FEATURE 984)

TO FORWARD ALL YOUR CALLS DIRECTLY TO VOICEMAIL.

IF YOU ARE GOING TO BE AWAY OR ARE BUSY PRESS THE FWD TO VM

BUTTON AND ALL YOUR CALLS WILL GO DIRECTLY INTO YOUR

VOICEMAIL AND WILL NOT RING ON YOUR PHONE.

TRANSFER TO VM: (FEATURE 986)

TO TRANSFER A CALL DIRECTLY TO SOMEONES VOICEMAIL.

ONCE YOU HAVE THE CALLER ON THE LINE PRESS THE TRANSFER TO VM

BUTTON AND ENTER THE MAILBOX # OF THE PERSON YOU WISH TO SEND

THE CALLER TO.  HANG UP.

INTERRUPT: (FEATURE 987)

VOICEMAIL INTERRUPT, THIS ALLOWS YOU TO INTERRUPT A CALLER

LEAVING YOU A MESSAGE.

PAGE: (FEATURE 60)

MAKE A PAGE ANNOUNCEMENT THROUGH EITHER THE INTERNAL CODE(1)

OR EXTERNAL CODE (2) SPEAKERS, OR BOTH CODE (3).  ZONE 0 PAGES ALL

ZONES.

CONFERENCE: (FEATURE 3)

ESTABLISH A CONFERENCE CALL BETWEEN YOURSELF AND 2 OTHER

PARTIES.

- MAKE OR ANSWER THE FIRST CALL

- PUT THE FIRST CALL ON HOLD

- MAKE OR ANSWER THE SECOND CALL

- AFTER THE SECOND CALL IS CONNECTED PRESS YOUR CONFERENCE BUTTON OR (FEATURE 3)

- PRESS THE LINE OR INTERCOM BUTTON OF THE FIRST HELD CALL

- PRESS THE RELEASE BUTTON TO END THE CONFERENCE CALL.

TO REMOVE YOURSELF FROM A CONFERENCE PERMANENTLY:

PRESS FEATURE 70.  THE OTHER 2 CALLERS REMAIN CONNECTED.

TO PUT A CONFERENCE ON HOLD:

PRESS THE HOLD BUTTON.  THE OTHER 2 CALLERS CAN STILL TALK TO ONE ANOTHER.

TO SPLIT A CONFERENCE:

PRESS THE LINE OR INTERCOM BUTTON OF ONE CALLER TO CONSULT PRIVATELY WHILE THE OTHER CALLER IS ON HOLD.  TO RE-ESTABLISH THE CONFERENCE PRESS FEATURE 3 OR YOUR CONFERENCE BUTTON.

TO DISCONNECT ONE PARTY:

PRESS THE LINE OR INTERCOM BUTTON OF THE CALLER YOU WANT TO DISCONNECT, THEN PRESS THE RELEASE BUTTON.  PRESS THE LINE OR INTERCOM BUTTON OF THE REMAINING CALLER TO RESUME YOUR CONVERSATION.

TO INDEPENDENTLY HOLD 2 CALLS:

PRESS THE LINE OR INTERCOM BUTTON OF THE FIRST CALLER, THEN PRESS THE HOLD BUTTON.  THE SECOND CALLER IS AUTOMATICALLY PUT ON HOLD. TO RE-ESTABLISH THE CONFERENCE, RETRIEVE ONE CALL FROM HOLD, PRESS THE CONFERENCE BUTTON OR FEATURE 3 THEN RETRIEVE THE SECOND CALL FROM HOLD.

SPEED DIAL: (FEATURE 0)

DIAL AN EXTERNAL TELEPHONE NUMBER USING A THREE-DIGIT CODE.

TO MAKE A CALL USING A SPEED DIAL CODE:

USER SPEED DIAL CODES ARE USED EXCLUSIVELY AT YOUR TELEPHONE

- PRESS FEATURE 0 OR YOUR SPEED DIAL BUTTON

- ENTER THE 3 DIGIT CODE FOR THE NUMBER

NOTE: THESE SPEED DIAL #’S WILL BE PUT IN BY THE SYSTEM ADMINISTRATOR AND YOU WILL BE GIVEN A LIST WITH SPEED DIAL CODES.

CALL TRANSFER: (FEATURE 70)

SEND A CALL TO ANOTHER TELEPHONE WITHIN YOUR SYSTEM, OR TO AN EXTERNAL TELEPHONE.  YOU MAY NOT BE ABLE TO TRANSFER A CALL ON AN EXTERNAL LINE TO AN EXTERNAL TELEPHONE, DEPENDING ON THE CAPABILITIES OF THE LINES.

- MAKE OR ANSWER A CALL

- PRESS THE TRANSFER BUTTON OR FEATURE 70

- CALL THE PERSON YOU WANT TO TRANSFER THE CALL TO

- STAY ON THE LINE IF YOU WISH TO SPEAK TO THE PERSON FIRST

- PRESS RELEASE TO COMPLETE THE TRANSFER

IF AN EXTERNAL CALL IS TRANSFERRED TO A BUSY INTERNAL OR NETWORK EXTENSION, OR IS NOT ANSWERED AFTER A FEW RINGS, THE CALL AUTOMATICALLY RINGS YOU BACK.

CALL PARK: (FEATURE 74)

PUT A CALL ON HOLD SO THAT IT CAN BE PICKED UP FROM ANY TELEPHONE IN YOUR SYSTEM.  THE DISPLAY SHOWS A 3 DIGIT RETRIEVAL CODE.  TO RETRIEVE A PARKED CALL FROM A TELEPHONE, PRESS AN INTERCOM BUTTON AND DIAL THE RETRIEVAL CODE.

VOICE CALL: (FEATURE 66)

MAKE A VOICE ANNOUNCEMENT OR BEGIN A CONVERSATION THROUGH THE SPEAKER OF ANOTHER TELEPHONE WITHOUT FIRST MAKING THE OTHER TELEPHONE RING.

LAST # REDIAL: (FEATURE 5)

DIALS THE LAST # THAT YOU DIALED.

CALL QUEUING: (FEATURE 801)

ANSWER THE NEXT CALL.  IF MORE THAN ONE CALL IS WAITING PRIORITY IS GIVEN TO INCOMING EXTERNAL CALLS OVER CALLBACK, CAMPED OR TRANSFERRED CALLS

INTERCOM:

THESE BUTTONS ALLOW YOU TO MAKE AN EXTERNAL CALL BY PRESSING 9 AND THEN DIALING THE PHONE #.

THEY ARE ALSO USED TO RECEIVE INTERNAL AND EXTERNAL CALLS AND TO PICK UP A PARKED CALL.

HANDSFREE/MUTE:

ALLOWS YOU TO TALK WITHOUT PICKING UP YOUR RECEIVER

AUTODIALS:

EXTERNAL #:  TO PROGRAM AN EXTERNAL TELEPHONE # ON A BUTTON ON YOUR PHONE.

PRESS FEATURE * 1 THEN PRESS THE BUTTON YOU WANT TO PROGRAM AND PRESS AN INTERCOM BUTTON PRESS 9 (IF YOU HAVE TO DIAL 9 TO GET AN OUTSIDE LINE) THEN ENTER THE TELEPHONE # YOU WANT TO PROGRAM.

INTERNAL: TO PROGRAM AN INTERNAL # ON A BUTTON ON YOUR PHONE.

PRESS FEATURE * 2 THEN PRESS THE BUTTON YOU WANT TO PROGRAM AND ENTER THE EXTENSION #

FEATURE CODES: TO PROGRAM A FEATURE CODE ON A BUTTON ON

YOUR PHONE.  PRESS FEATURE * 3 THEN PRESS THE BUTTON YOU WANT

TO PROGRAM AND ENTER THE FEATURE CODE.